## Slide 1: Modules and Applications

## Slide 2: iCub Modules
The software architecture is made of modules: a module is an executable that performs a specific task, and whose interface is defined in terms of YARP ports
Granularity at this level is quite fine
Behaviors are obtained by instantiating and connecting networks of modules

## Slide 3: Modules and Applications
An application is a logical collection of modules with a particular purpose (e.g. attention system, reaching, learning of affordances, drumming interaction history…)
In practice it is just a collection of configuration files and a text description in xml

## Slide 4: Writing Good Modules
Executable with yarp interface
Command line configuration:
  Algorithm parameters
  Port names
  Initialization files
Independent of working directory
Smooth shutdown

## Slide 5: The ResourceFinder class
Usage example :
random –robot icub –part head –joint 0
random –from random.ini
random.ini
robot icub
part head
joint 0

## Slide 6
Use a certain policy to locate random.ini
The “ICUB_ROOT” policy in short:
  locally in the working directory
  relative path if the name contains path information (as in: ../../mypath/random.ini)
  check in the $ICUB_ROOT/app/context
intuitive behavior
to support automation, reuse and deploy

## Slide 7: Changing the context
The context is a directory inside the “app” structure that stores all configuration files for a set of modules
Consider the following examples:
random –from random.ini –context learnHeadKin/conf
random –from random.ini –context learnArmKin/conf

## Slide 8: The code
ResourceFinder rf;
rf.configure(“ICUB_ROOT”, argc, argv);
configuration, set the policy to use, pass command line parameters

## Slide 9: The code
ResourceFinder rf;
rf.configure(“ICUB_ROOT”, argc, argv);
ConstString robotName=rf.find(“robot”).asString();
ConstString partName=rf.find(“part”).asString();
int joint=rf.find(“joint”).asInt();
query parameters…

## Slide 10: RF Configuration
Choose the policy to use:
ResourceFinder rf;
rf.configure(“ICUB_ROOT”, argc, argv);
The policy is specified in a txt file (ICUB_ROOT.ini), located with certain rules (e.g. $ICUB_ROOT, but also in /etc, this can be extended)
The policy file describes the rule used by the ResourceFinder

## Slide 11
The “ICUB_ROOT” policy in full:
  locally in the working directory
  relative path if the name contains path information (as in: ../../mypath/random.ini)
  check in the $ICUB_ROOT/app/context
  if $ICUB_ROBOTNAME exists check $ICUB_ROOT/app/$ICUB_ROBOTNAME/conf
  check $ICUB_ROOT/app/default/conf
intuitive behavior
to support automation, reuse and deploy

## Slide 12: Simplify usage: default values
You can set defaults for context and configuration files:
rf.setDefaultConfigFile(“random.ini”);
rf.setDefaultContext(“learnHeadKin/conf”);
Consider these examples:
random //use default config and context
Use default config, change context:
random –context learnHeadKin/conf
Change config and context:
random –from myRandom.ini –context learnArmKin/conf

## Slide 13: Why a ResouceFinder
Modules are working directory agnostic, easier to use in case of
  remotization
  release/install
Preserve “local” behavior for developers, intuitive behavior when config files are local w.r.t to the process working directory
Easy to switch context, when the module is used in different applications
A single class/policy manages access to resources: flexibility

## Slide 14: Further readings
Specifications:
  Manual: Configuration and Resource Files
See eris.liralab.it  Tutorials:
  How to organize the command line parameters…
  How to organize … advanced tutorial

## Slide 15: The RFModule class
You create a new module by deriving a new class from RFModule
class MyModule:public RFModule
{
public:
bool configure(ResourceFinder &rf)
{ //module configuration }
bool close()
{ //code executed at shutdown }
};
MyModule module;
ResourceFinder rf;
//configure resource finder
module.runModule(rf); //if configure returns true block here until the module closes
get parameters form RF and configure the module, return true on success, false otherwise
perform cleanup, close ports, delete memory
all as in previous slides

## Slide 16
What does a module do?
Nothing, really…

## Slide 17
What does a module do?
Nothing, really…
Wait for termination signal (ctrl-c or signal from yarprun)
Can be configured to receive messages from a port/keyboard
Can perform periodic activities
It is a container for active objects (threads)

## Slide 18: Attach callbacks
class MyModule::RFModule
{
Port handlerPort;
…
bool configure(ResourceFinder &rf)
{
// use rf to configure your module
attachTerminal(); //attach terminal
handlerPort.open(“/myModule”);
attach(handlerPort);
…
}
…
}

## Slide 19
Now add a respond message to catch data from terminal or/and the handler port
// Message handler. Just echo all received messages.
bool respond(const Bottle& command, Bottle& reply)
{
cout<<"Got something, echo is on"<<endl;
if (command.get(0).asString()=="quit")
return false;
else
reply=command;
return true;
}

## Slide 20: Periodic Activities
In MyModule overload:
double getPeriod()
{ return 1; }
bool updateModule()
{
// place here code that will be
// executed every “getPeriod” seconds
return true;
}
define period in seconds
this function will be executed until termination

## Slide 21
You can interrupt blocking reads on ports in the interrupt method:
bool interruptModule()
{
port1.interrupt();
port2.interrupt();
…
return true;
}

## Slide 22: Further readings
See tutorial at:
  eris.liralab.it  Tutorials  Using the module helper class..
YARP online documentation about the RFModule class
Consider using the thread classes:
  eris.liralab.it  Tutorials  How to write a control loop using threads

## Slide 23: Yarprun
A server for running executables remotely
Why not ssh?
Usage:
  On server side: yarprun –server /nodename
  On client side: yarprun –cmd “mymodule” –on /nodename
Other features: io redirection, sig term/sig kill, check termination

## Slide 24: Defining applications
Applications are described using xml
Through YARP the application manager performs common tasks e.g. starting modules with correct parameters, connect and disconnect ports, check dependencies
OS independent remote execution, with i/o redirection
…
…
.xml

## Slide 25: An example:
<application>
<name>Test grabbers</name>
<dependencies>
<port> … </port>
</dependencies>
<module>
<name>yarpdev</name>
<parameters>--device grabber --subdevice test_grabber --name /test1</parameters>
<node>pc1</node>
<stdio>pc2</stdio>
<tag>test-grabber1</tag>
</module>
<module>
…
</module>
<connection>
<output>/test1</output>
<input>/view1</input>
<protocol>tcp</protocol>
</connection>
</application>